Understanding the Atmospheres of Hot Earths and the Impact on Solar System Formation
Observations

---
Outline:
1) What has been found-
i) Planets
ii) Characterization Techniques
iii) Properties of planets.
2) What our strategy is-
i) Observing
ii) Image processing

---
A little history
The first extrasolar planet detected was published in 1992: Wolszczan & Frail detected two planets of 2.8 and 3.4 Earth masses (the first superEarths!) orbiting a pulsar.
This system now has 3 planets (4 possibly) with the smallest having 0.02MEarth
That's 1.8 Lunar masses!

---
A little history
These planets were discovered by using variations in the arrival times of the pulsar pulses.
This pulsar has a period of 6.2 milliseconds and so arrival times can be determined with great accuracy.

---
The first extrasolar planet around a 'normal' (main-sequence) star was discovered in 1995 by Swiss astronomers.
The planet has M=0.5MJupiter and orbits in 4.2 days. It was discovered via Doppler shifts in the host star's spectrum- the RV method

---
The first extrasolar planet around a 'normal' (main-sequence) star was discovered in 1995 by Swiss astronomers.
The planet has M=0.5MJupiter and orbits in 4.2 days. It was discovered via Doppler shifts in the host star's spectrum- the RV method

---
The RV method used a new technique of observing through an iodine cell.
BUT... this method only works for bright stars and is biased towards massive planets in short orbits at low inclinations, which produce the highest velocities.

---
And this was largely the state of things for the next 15 years.
About 300 planets were discovered.
Improvements in the RV method detected planets down to about 8 Earth masses in very short orbits.

---
Transits of a few (already known) planets were detected from Earth.

---
A few planets were detected using microlensing.
These events do not repeat.

---
These are all indirect methods!
The planet itself is not measured, only its effect on the host star.

---
Direct imaging: currently works for big planets far from their host stars.
Fomalhaut b is 2MJ, 115 AU from its host star.

---
Kepler began taking data in March 2009, and now there are
nearly 3,900 planet candidates!
Kepler has used the transit method, while staring at 150,000+ stars.

---
This has been the tipping point.
There are now so many planets that we can do some statistics.

---
12.8%
29.8%
47.1%
7.4%
42.6%
3.0%

---
Planets we may be interested in.
10MEarth

---
Not in the previous graphs
(no mass estimates)
POrb= 13 21 40 days
aAU= 0.10 0.14 0.21 AU
Mercury's orbit is 88 days at 0.39 AU.

---
387 of 713 (54%) planets have orbits smaller than Mercury's

---
Characterization Techniques
Orbit: Mass and Radius
Transmission Spectroscopy
Reflection Spectroscopy (including broadband photometry)

---
Masses come from orbital mechanics only. Typically this is Doppler shift.
Occasionally from orbital period and semimajor
axis.
The mass of the planet must be assumed (astero- seismology can help). Inclination is a free parameter.

---
Transits also constrain the inclination:
but for very short period planets, the constraints are lessened.

---
Doppler plus astrometry can constrain the inclination.

---
Transits also give the planet's radius.
Again asteroseismology can help.

---
With sufficient transit precision (ingress/egress timings), inclination can be determined too (and more precise radii).

---
With mass and radius come density.
Model comparisons can be used to infer bulk composition.

---
But the model dependence is large and open to some interpretation.

---
Transmission spectroscopy is a more direct means of detecting the planet- but only the atmosphere.

---
But of course the planet's contribution has to be separated from the star's contribution- and this is difficult.

---
Note that mostly these are not true spectra.
They are multi-filtered data compared to synthetic, or lab, spectra.

---
Reflection Spectrum: Differenced from the star.

---
At different orbital phases, the amount of light received from the planet changes.
Each filter, which is a summed portion of the spectrum, will depend on the amount of reflected starlight (albedo) and the planetary contribution (blackbody + emission).
Rouan et al. 2011

---
At different orbital phases, the amount of light received from the planet changes.
In transiting systems, at some phases (secondary eclipse), there is starlight only (the planet is behind the star), which can be compared to other phases, where the planet contributes.
Rouan et al. 2011

---
Then there is wavelength-dependent albedo.
This is what makes planets different “colors”.

---
Combined, you get color and phase dependent reflection
Rouan et al. 2011
hot-vs-cold Jupiter

---
You can also get phase dependent thermal emission.
Rouan et al. 2011

---
This is how the 'blue' planet was found(?)

---
Actual measurements
Conclusions
from
Evans et al. 2013

---
I'll come back to this in the context of lava planets and magma oceans.

---
2002: Sodium detected
2003: H2 detected
2004: O2 & C & 3Rp atmo and tail indicating evaporating atmosphere.
2007: Balmer series & jump detected, providing the picture at left.
All HST UV/nUV
transmission
spectroscopy.
A Hot Jupiter

---
Findings and speculations for hot (super)Earths that we're interested in.

---
Model transmission spectra for H-rich (blue), H-poor (green) and intermediate H (red) atmospheres for a hot SuperEarth.
Spitzer bands shown as points.

---
HST transmission spectroscopy determined that the atmosphere is optically thick for GJ1214b (R=2.7REarth
Berta et al. 2011)
Water Clouds

---
Overall, GJ1214b's IR transmission spectrum is consistent with H2O.

---
As is the reflection spectrum. From Spitzer: Gillon et al. 2013
Note that there are 2 data points!
At 3.6 and 4.5 microns.

---
GJ1214b is a hot Super-Earth:
Mass = 6.5 MEarth
Radius = 2.7 REarth
r = 1.6 +/- 0.6 g/cc
(Anglada-Escude et al. 2013)
BUT... a side note that CFHT WIRCam observations indicate a H/He atmosphere inconsistent with a water world. (Croll et al. 2011; transmission spectra)

---
Their conclusion!

---
55 Cnc e
M=7.8MEarth R=2.17REarth
Density downgraded to 4.78+1.31-1.20g/cc (Demory 2011)
Steamy water atmosphere?

---
55 Cancri e: Now fortified with Carbon!
M~8MEarth, R~2.2REarth, Porb=18 hours T~2,400K
(Madhusudhan et al. 2012)

---
The planet is primarily composed of carbon as graphite and diamond; iron; silicon carbide; and possibly some silicates

---
The star is carbon-rich, so the protostellar disk was also likely to be.

---
Graphite over diamond over silicon-based minerals over iron core. Hot side ~2,400K.

---
CoRoT-7b
M=7.42MEarth R=1.58REarth
r = 10.4 +/- 1.8 g/cc
Kepler 10b
M=4.5MEarth R=1.4REarth
r = 8.7 g/cc
Both claimed as Fe-rich Mercury-like from structural models only (Gong & Zhou 2012 and Wagner et al. 2012).

---
Kepler 10b:
The lightcurve is measured around the orbit (at right) and a model is generated (above)
The model is essentially a 2-parameter fit: albedo and thermal radiation; assuming negligible atmosphere, constant albedo, and the emissivity of liquid alumina.
(Rouan et al. 2011)

---
Reflected (blue) and thermal emission (red) for a=0.5 just outside of secondary transit.
Assumes night side is cold and (fitted- Bruce?) day side reaches 3000K

---
Kepler 11 has 6 planets, 5 with orbital periods under 50 days.
But all with low densities.
(Lissauer et al. 2013)

---
Our Strategy (so far)

---
Observe several star/planet systems with varying sized planets (from superJupiters down to
superEarths) at several orbital phases.
This is done in several filters from Sloan u (where thermal emission from the planet should be zero) to I (where thermal emission may contibute).

---
Build up the phase-dependent lightcurve (like at right) and compare with models.
Use color-color diagrams as diagnostics.

---
Color-color predictions for Gaseous planets.
(from Cahoy, Marley, & Fortney: NASA Ames)
The streaks indicate orbital phase from 0 (behind, but not obscured) to 180 (illuminated side away from observer) as they fade away.

---
Another one from the same paper but with more filter combinations.
Note that these are all optical.
(I is Bessell I, just like we're using and is very near-IR)

---
Initially, we thought we'd use GTCam2 and simultaneously plug away in 3 colors; taking a ton of images!
However, the lack of comparison stars is an issue.

---
So we're using our other CCD camera and flipping filters.
The FoV is 4 times larger so we get many more comparison stars.

---
The End